## Slide 1: A Hybrid Quantum-Classical CNN Architecture for Semantic Segmentation of Radar Sounder Data
Raktim Ghosh
Amer Delilbasic
Gabriele Cavallaro
Francesca Bovolo
E-mail: raghosh@fbk.eu

## Slide 2: Outline
Introduction and Motivation
Problem Statement
Preliminary Results on Radar Sounder Data
1
Conclusions & Future Work
Proposed Hybrid Quantum-Classical Architecture
2
3
4
5

## Slide 3: Introduction
Research activities have been carried out in the development of different types of Quantum Computers (QC), that incorporates principles of quantum computing to perform computations on qubits.
By utilizing the principles of QC, quantum algorithms address miscellaneous tasks such as quantum simulations, search and optimizations, quantum cryptography, etc.
In the domain of radar sounder, the data volume is large (e.g., SHARAD, MCoRDS) and will increase because of new operated instruments (e.g., RIME on JUICE).
Recently, Classical CNN and Transformers-based approaches have been developed to segment radar sounder data.
However, no attempt has been made to leverage the quantum related concepts in processing radar sounder data.
Notes: Automatic vs visual inspection:
Objective vs subjective (misinterpretations)
Quantitaive vs qualitative (not reproducible)
Fast vs Time consuming
Cost of cluster vs cost of exter

## Slide 4: Radar Sounder
Radar Sounder technology
Transmitted EM pulses at low frequency (MF/HF/VHF) and with a wide band.
Wave penetrates the subsurface and at each dielectric discontinuity, a part of the EM wave is reflected back.
Radargram
A radargram is the coherent representation of backscattered echoes.
From a radargram it is possible to characterize subsurface target structures and estimate relevant parameters (i.e., dielectric properties, depth).
Radargram acquired in Greenland by MCoRDS
Azimuth
Range
Bedrock
Internal Layers
Noise

## Slide 5: Problem Statement and Goal
Let us denote a radargram as:
Goal: to develop a hybrid supervised segmentation model using Hybrid Quantum-Classical (HQC) CNN architecture that assigns a distinct class to each pixel in R(i,j).

## Slide 6: Hybrid Quantum-Classical Architecture
Input Training
Samples
Successive CNN Layer with Max pooling
HQC Bottleneck Quantum Layer
Quantum Circuits - Bellman and Real Amplitudes Circuit
Hybrid Quantum-Classical Encoder
HQC Decoder
Quantum Embedding
Loss Function
Successive Transpose Convolutions Operations to recover the Spatial Dimension
{(Xn Ln), n=1,..., N}

## Slide 7: Hybrid Quantum-Classical Architecture
Convolutional Layers are used to encode the information to a latent space with reduced spatial dimension.
The information in the latent space is injected into the quantum circuits for estimating the probability amplitudes.
The probability amplitudes are utilized as an input to the Decoder to upsample the spatial dimension for the final predictions.
Schematic layout of HQC Architecture

## Slide 8: Schematic Layout of the Hybrid Architecture
CNN
TC
C1
TC
TC
C2
C3
C4
C5
C0
QC Layer
TC - Transpose Convolution
16
32
64
1024
FC
FC
4
16
1024
64
32
16
Ci - ith convolution operation

## Slide 9: HQC Bottleneck Quantum Layer
The Circuit prepares an Entangled state by utilizing the Hadamard and CNOT Gates.
After the rotated entangled state, the CNOT processes are mirrored.
The qubits are passed through corresponding Hadamard Gates with succeeding rotation gates.
The mutual entanglements are established with succeeding rotation gates.
[1] - Bellman Quantum Circuit
[2] - Real Amplitude Quantum Circuit

## Slide 10: Experimental Setup
Noise
Parameters | Values
Number of Training Samples | 800
Number of Testing Samples | 254
Size of the Individual Samples | 50 * 50
Batch Size | 16
Number of Epochs | 50
Learning Rate | 0.00001
Optimizer | AdamW
Sample radargrams acquired by MCoRDS3 Sensor (NASA)
Azimuth
Range
Bedrock

## Slide 11: Qualitative Results
Azimuth
Range
Radargram
Reference
Classical
Bellman
Real Amplitudes
Noise
Bedrock
Qualitatively, the proposed HQC architecture accurately distinguishes the bedrock from the noise.
The classical counterpart was unable to distinguish bedrock from noise.
Proposed HQC approach

## Slide 12: Quantitative Results
Algorithms | F1-Score | OA
HQC (Real Amplitudes Circuit) | 0.8477 | 93.93
HQC (Bellman Circuit) | 0.8248 | 93.13
Classical Architecture | 0.7407 | 89.55
The proposed architecture with the Real Amplitude Circuits achieved the highest rate of accuracy in terms of OA and F1-score.
F1-score improved 11% for Bellman Circuit and 14% for Real Amplitudes Circuit.
The quantum circuits as bottleneck connectors established a rich back-and-forth information processing system for the UNet-like architecture.
The contextual richness was decreased while using FC layer for the bottleneck connector as a counterpart of quantum circuits.

## Slide 13: Conclusions & Future Work
Conclusions
We developed a Hybrid Quantum-Classical CNN architecture for radargram segmentation.
The architecture incorporates Quantum Circuits as a bottleneck between the Encoder and Decoder.
The method depicts a rich contextual discriminative information transfer between the Encoder and Decoder.
Future Work
Replace the classical skip connectors with quantum layers for the UNET-like architecture in miscellaneous parts of the overall HQC settings.
Explore the unsupervised settings with the Quantum Circuits.
Notes: pubblicazioni